## Slide 1: CE 3372 water systems design
LeSSON 3: DEMAND ESTIMATION

## Slide 2: outline
Water Demand(s)

## Slide 3: Water supply demands
Uses
  Withdrawl
    Removal from stream, lake, or aquifer to supply user(s) – water is moved to satisfy the use
  Non-Withdrawl
    On-site uses for navigation, recreation – water can stay in same location to satisfy use
  Consumptive
    Fraction of withdrawl that is no longer available for further use – incorporated into crops and animals (actual biomass); industrial processes (heat exchange)

## Slide 4: Water needs for a city
Consider some generic urban area
  Municipal Requirements
  Large Industrial Requirements
  Waste Assimilation Requirements

## Slide 5: Municipal requirements
The municipal requirements are related to the number of users by means of the simple relation:
Where V=volume, P=population, V/P = volume per person (used).

## Slide 6: Population forecasting (graphical)
Short-term forecasting
  Declining growth
  Arithmetic growth
  Geometric growth
Same arithmetic as substrate limited growth that you learn in Envriomental Engineering

## Slide 7: GEOMETRIC growth (mathematical)
When the growth curve is in the exponential phase
Where KP is the exponential growth constant

## Slide 8: Arithmetic growth (mathematical)
When the growth curve is roughly a straight line, then
Where KA is the slope of the growth curve

## Slide 9: DECLINING growth (mathematical)
When the growth curve approaching the carrying capacity of the region
Where KD is the declining rate constant

## Slide 10: Longer-term Forecasting
Naturally, none of the constants are convienently tabulated and historical census data are used both for short term forecasts – the US Census Bureau makes estimates of census values between the every decade census.
If the region has been around awhile (in the population sense) then the plot might be strightforward to construct.
Longer term adds the ratio and correlation techniques and component techniques

## Slide 11: comparison forecasting
Geographically similar areas are used and projections are made by comparing these growth curves to the area of interest.
Uncertainty that area of interest may not progress similarily to past growth of comparision areas.

## Slide 12: Forecasting (Ratio/correlation)
Ratio (transposition) method is based on the ratio of observed populations of two study areas.
Correlation method fits (ordinary least squares on the populations or log-populations) to generate a predictive equation based on a reference population.

## Slide 13: Forecasting (component)
Formal model of a population that considers birth rate (B), death rate (D), net migration rate (M) over a forecasting interval
Non-trivial modeling activity
Nice introduction to the mathematics in: Frauenthal, J.C. 1980. Introduction to Population Modeling. Birkhäuser, Boston, Basel, Stuttgart 186p. ISBN 3-7643-3015-5

## Slide 14: Water usage
The forcasting helps establish the target population to be served, next the use per person needs to be established.
Components include:
  Avergae Daily Demand (by user category)
  Hourly Variation
  Fire Demand

## Slide 15: Per capita water usage – design life
Design life varies by system component (or statute).
Maintenance/replacement needs to be planned for components that will fail within the overall design (service) life

## Slide 16: Major components
Components differ by system type.
For example consider the two systems in the figure – there are some common components, however each system will have unique components to consider.

## Slide 18: Average daily usage
Residential
  Water for drinking, landscape, swimming, fires, street cleaning, etc.
  Usually two demand peaks (morning and evening)
Commercial
  Motels, hotels, offices, shopping centers
  Usually less peak demand and less varied than residential
Industrial
  Water for fabrication, cooling, petroleum refining, etc.
  Water use depends on type of industry
Notes: When industrial requirements are relatively important (major user) they are usually considered separately

## Slide 19: Average daily usage
Estimation tools:
  USGS Circular 1200
  Authorative sources
  Approximation (for preliminary design)
  Per-connection calculation

## Slide 20: USGS Circular 1200
Contains maps and tables by location
Useful gross estimate tool

## Slide 21: Average daily use (approximations)
Water Distribution Systems "Water Distribution Systems" in Land Development Handbook, Ed. S.O. Dewberry, Dewberry Inc., McGraw-Hill -- has tables similar to:

## Slide 22: Per-connection (Plumber Estimate)
How Much Water Can You Actually Get?
  Flow Rates are measured in gallons per minute (gpm).
  For our purposes, we will talk about the amount of water that you can get through a pipe at a velocity of 8 feet per second (a standard velocity used to engineer a plumbing system).
Plumbing diameter will limit the flow rate you can get – the larger the pipe, the more water you can get. A home with 1″ plumbing can use substantially more water than a home with 3/4″ plumbing.
Meter to house
Inside home

## Slide 23: Per-connection (Plumber Estimate)
1. Think about the maximum number of fixtures and appliances you might operate at the same time.
2. Look at the chart to see how many gallons per minute each device requires.
3. Add up the flow rates for all the devices you selected.
You just figured out the PEAK FLOW RATE that you need.
Now, think about your continual water use, or water use that may run for more than 10 minutes. Add up the fixtures again, and you just calculated your SERVICE FLOW RATE.

## Slide 24: Per-connection (Rural Estimate)
http://extension.psu.edu/natural-resources/water/drinking-water/best-practices/water-system-planning-estimating-water-use

## Slide 25: Per-connection (TCEQ)

## Slide 26: Usage variation (within a day)
The average estimates are for long-duration (years) usage.
Use changes with seasons, days within a week, and special cases (the big flush at half-time during the Superbowl)

## Slide 27: Usage variation (within a day)
In absence of any supporting data one can employ a rule-of-thumb estimate
T is in units of days. The rule-of-thumb is intended for use over a time frame for 1 hours up to 365 days.

## Slide 28: Fire demand
Fire usage on an annual basis is probably negligible, but when fire demand arises the rate of withdrawl is high.
Designers are required to design and build the system to be able to provide fire demand (hence service reservoirs will have excess capacity expressly to supply fire flow!)

## Slide 29: Fire demand
Required flow rates are by:
  Statute (consider the requirement in the Houston IDM for a fire hydrant)
  Insurance organizations, for example:

## Slide 30: Industrial demand
Large industries usually supply their own water
If the community will supply the industry, then industrial requirements will need to be estimated.
Industry | Average Water Usage
Thermal Power | 80 gal/kWh
Steel Production | 35,000 gal/ton
Paper Production | 50,000 gal/ton
Textile Production | 140,000 gal/ton
Carbon (Coke) Production | 3,600 gal/ton
Petroleum Refining | 770 gal/barrel

## Slide 31: Waste assimilation demand
Treated (or even untreated) wastewater is eventually discharged back into the environment and this demand for assimilative capacity needs to be estimated.
Many methods are employed – TMDL, DO Sag, and similar modeling approaches.
Preliminary values can be estimated by a simple linear relationship

## Slide 32: Irrigation demand
Irrigation (Agricultural) – outside scope of this class but use categories are:
  Biomass (how much is bound in the actual crop)
  Evapotranspiration – Consumptive
  Farm Losses
  Conveyance Losses

## Slide 33: other demands
Hydropower
  Run-of-river
  Storage release
Navigation
  Regulation of river
  Artificial canal
  Lock-and-Dam