## Slide 1
CE 3372 water systems design
Pumps and lift stations –Part 1 (fall 2020)

## Slide 2: Pumps
A mechanical device that transfers mechanical energy into a liquid; used to
  Lift from lower to higher elevation Lift stations
  Increase pressure Booster stations
Gas phase equivalent
  Compressor
Pump
Motor
suction
discharge

## Slide 5: Pumps
Positive (Fixed) Displacement Pumps
  Fixed volume of fluid is displaced each cycle regardless of system static head/pressure
  Lower flow rates and higher head than non-positive pumps
Variable Displacement Pumps
  Varying volume of fluid is displaced dependent on system static head/pressure (back pressure)
Notes: 2 principle types of plants

## Slide 6: Pumps
Fixed Displacement Pumps
  Screw Pumps
  Reciprocating Pumps
Variable Displacement Pumps
  Centrifugal (Radial-Flow) Pumps
  Propeller Pumps (Axial-Flow)
  Jet Pumps (Mixed-Flow)
Notes: 2 principle types of plants

## Slide 7: Positive Displacement Pumps
Screw Pump
  A revolving shaft with blades rotates in a trough at an incline and pushes water up
Notes: The auger catches a portion of water and lift it as the pump screw rotates.
The diameter, fill depth, pump angle, etc are determinants of pump charact.
Commonly used in wastewater lifting and hurricane barrier lifting
Very tolerant of debris in liquid. Failure is HUGE

## Slide 8
Positive Displacement Pumps
Progressive Cavity Pump
  A revolving shaft (rotor) with rotates in a trough (stator)

## Slide 9: Positive Displacement Pumps
Reciprocating Piston Pump
  A piston sucks the fluid into a cylinder and then pushes it out
Notes: Upstroke, chamber fills. Downstroke, liquid is pushed out
Check valves prevent back flow.
Bore diameter, stroke length and rate are principal det of the operating character of a piston pump.
If no flow can occur, discharge is blocked, piston pump can and will destroy !!

## Slide 10: Pumps
Fixed Displacement Pumps
  Screw Pumps
  Reciprocating Pumps
Variable Displacement Pumps
  Centrifugal (Radial-Flow) Pumps
  Propeller Pumps (Axial-Flow)
  Jet Pumps (Mixed-Flow)
Notes: 2 principle types of plants

## Slide 11: VARIABLE Displacement Pumps
Classification is based on the way water leaves the rotating part of the pump
  Radial-flow pump – water leaves impeller in radial direction
  Axial-flow pump – water leaves propeller in the axial direction
  Mixed-flow pump – water leaves impeller in an inclined direction (has both radial and axial components)
Notes: Propeller creates thrust
Impeller creates suction

## Slide 12: Radial-Flow Pumps
Centrifugal Pump
  Accelerates water using an impeller
https://www.youtube.com/watch?v=BaEHVpKc-1Q
https://www.youtube.com/watch?feature=player_detailpage&v=ECv1VwW6RTo#t=122
Discharge
Suction (Eye)
Notes: Play til 3:11
Rate of impeller is how much momentum it can transfer to the water
Conversion of rotational kinetic energy to hydrodynamic energy of fluid flow
Cent pump can be submersible wet or dry

## Slide 13: Axial Flow Pumps
Axial flow pumps have impellers whose axis of rotation is collinear with the discharge
Used in high flow, low head applications
suction
discharge
Notes: Moving the same axis the fan rotates on.
Collinear enough.
Perpendicular to blade