## Slide 1: CE 3372 water systems design
LeSSON 8: hydraulics of networks

## Slide 2: outline
Network Hydraulic Principles
Constructing the Network System of Equations
  Link-Node Continuity Partition
  Link-Node Energy Partition
Adding Pumps

## Slide 3: Network Hydraulic principles
Conservation of mass at a junction
  SInflow – SOutflow = 0 (at a node)
    Positive demand at a node is an outflow
    Negative demand (injection into the network) is an inflow
    One balance equation for each node
  Head has a single value
    Usually expressed as a pressure
    Visualize as height of column of water in a piezometer at the junction
Pressure Head
Piezometer
Inflow
Outflow
Demand (External)

## Slide 4: Network Hydraulic principles
Datum
Conservation of energy along a conduit
  Modified Bernoulli’s equation
  Include fitting losses if known
One energy equation for each conduit (link)
Pressure Head
Elevation Head
Head Loss

## Slide 5: Branched System
Distribution networks are multi-path pipelines
                One topological structure is branching
                One node (continuity)
                Three links (energy)
                Four unknowns: VAD,VBD,VDC,HD

## Slide 6: Branched System - analysis
Head loss in each pipe
Continuity at the node

## Slide 7: Branched System
4 Equations, 4 unknowns
Non-linear so solve by
    Newton-Raphson
    Quasi-Linearization
Quadratic in unknown, so usually can find solution in just a few iterations

## Slide 8: Looped System
Looped system is where one or more pipes rejoin at a different node.

## Slide 9: Looped System
Nodes:
      Inflow = Outflow
      Energy Unique
Links
      Head loss along pipe
      Head loss in any loop is zero
LOOP

## Slide 10: Example – branched system

## Slide 11: Example – branched system

## Slide 12: Example – branched system

## Slide 13: Example – branched system

## Slide 14: Example – branched system

## Slide 15: Example – branched system

## Slide 16: Example – branched system

## Slide 17: Example – looped system

## Slide 18: Example – looped system

## Slide 19: Example – looped system

## Slide 20: Example – looped system

## Slide 21: Example – looped system

## Slide 22: Example – looped system

## Slide 23: Example – looped system

## Slide 24: Example – looped system

## Slide 25: Example – looped system

## Slide 26: Example – looped system

## Slide 27: Networks
Branched and looped systems are called networks
      Multiple paths for water to flow in the system
        External “demands” are applied at nodes
        External “supply” is treated as negative demand

## Slide 28: Networks
Analysis techniques
  Hardy-Cross (Loop Only Equations)
  Newton-Raphson (Node+Loop Equations)
  Hybrid Method (Haman and Brameller (1971))(Node+Pipe Equations)
    Build node and pipe equations (LIKE THE BRANCH SYSTEM)
    Then solve the SIMULTANEOUS non-linear system for flows and heads

## Slide 29: Networks
Consider the system below

## Slide 30: Networks
Six pipes
4 nodes + 1 RESERVOIR (Fixed grade node)
Demands shown at nodes
Flow arrows for sign convention

## Slide 31: Networks
Continuity is written at nodes (node equations).
Energy loss (gain) is written along links (pipe equations).
The entire set of equations is solved simultaneously.

## Slide 32: Networks
Define an unknown vector (X)

## Slide 33: Networks
Build the node and pipe equations

## Slide 34: Networks
Build the node and pipe equations

## Slide 35: Networks
Build the node and pipe equations

## Slide 36: Networks
Build the node and pipe equations

## Slide 37: Networks (HYBRID METHOD)
Continuity is written at nodes (node equations).
Energy loss (gain) is written along links (pipe equations).
The entire set of equations is solved simultaneously.

## Slide 38: ADDING PUMPS
A pump is treated as a link that adds head in a predetermined flow direction rather than removing head
So it will replace a link equation somewhere in the network model
Typical equation structure is

## Slide 39: Network analysis with a pump
Use the prior example as the network, but will replace the supply pipe with a pump and see how that changes the system of equations that need to be solved.

## Slide 40: Network analysis with a pump
Pump Curve

## Slide 41: Network analysis with a pump

## Slide 42: Network analysis with a pump
The actual pump curve function is built in a similar fashion as the loss terms from the previous lesson.
Again sign conveys direction
We should test for the implicit divide-by-zero that can occur as Q=0, and just use the shutoff head at that value

## Slide 43: Network analysis with a pump
Here is how the “equations” change : Original Problem

## Slide 44: Network analysis with a pump
Here is how the “equations” change : Change Supply Head
-0

## Slide 45: Network analysis with a pump
Here is how the “equations” change : Change Supply Pipe to Pump
Insert Head Function

## Slide 46: Network analysis with a pump
Here is how the “equations” change : New Model Equations

## Slide 47: Network analysis with a pump
Now, encode the new model into a solution tool and proceede.

## Slide 48: Networks – Why Model?
What is the flow distribution if the demands are changed as shown?
0.1 cfs
0.4 cfs

## Slide 49: Network modeling protocol
Sketch the network
    Label the nodes, links, supply, and demands
Build the node-arc incidence equations
    Continuity at each node
Build the pipe head-loss equations
    Head at start node, minus head loss equals head at end node
Build and run a computation tool (spreadsheet)
    Make an initial guess of flow rates
    Execute the computation tool, update guesses, continue until have flow balance and zero error term

## Slide 50: Network modeling protocol

## Slide 51: WHAT IF?
Once the tool is built, then “what-if” questions can be posed.
      What is the flow distribution if the demands are changed as shown?
0.1 cfs
0.4 cfs

## Slide 52
Once the tool is built, then “what-if” questions can be posed.
    As the network component count increases, the system of equations get big fast – A really complex problem would be beyond the practical limits of spreadsheet computing (the spreadsheet could do it, it would be hard to construct and maintain)