## Slide 1: CE 3372 Water Systems Design
Lesson 9: EPA-NET Introduction

## Slide 2: Introduction to EPANET
Introduction to EPANET
  Install on PC
  Install on Mac (Experimental; Unsupported)
Background on the program
  Interface tour
Example problem (from ES4) on EPANET

## Slide 3: System Components
Water source (Main Supply)
Lake
River
Aquifer
Treatment Facility
Transmission Lines
Pumping Facilities
Distribution Lines
Intermediate Storage Facilities
Treats and disinfects water
Meet water quality standards
Potable water
Convey water from source – treatment facility facility – network
Provide energy to move water
Stabilize line pressures
Reserve for peak demand periods
Provide storage for fire flow req.
Convey water from storage – service areas
Looped(grid) and Branched Layouts
Appurtenances
Fire Hydrants. Valves, auxiliary pumps, fittings

## Slide 4: Network Representation
Distribution network - Consists of items designed to convey potable water at adequate pressures and discharges
  Tanks
  Pumps
  Pipes
  Valves
  Fittings
  Meters
  Other appurtenences

## Slide 5: EPANET
Computer program that simulates flow in closed conduit (pressurized) systems
  Nodes
  Links (pipes, pumps, valves)
  Reservoirs (reservoir, tanks)
  Demand schedule (extended period simulation)

## Slide 6: Getting the Program
Download and install EPA-NET
  PC Users – Google EPANET or Use the class website
  MAC Users – Use the class website

## Slide 7: Getting the Documentation
Download and PRINT the user manual
  EPANET website, or class website.
    Topology constructed in a GUI
    Lengths, diameters, friction terms entered for each component (pipe, valve)
    Demand entered for each node (+ outflow, - inflow)

## Slide 8: About the program
Topology (Network Layout) is constructed in a GUI
Nodes
  Demand entered for each node (+ outflow, - inflow)
  Elevation for each node (to calculate pressure)
Links
  Lengths, diameters, friction terms entered for each component.
  Pipes, Pumps, Valves are all “link” components
Reservoir/Tank
  All models need a reservoir or tank (like the ground in an electric circuit)

## Slide 9: Stuff you Have to Choose
Head Loss Models
  Darcy-Weisbach
  Hazen-Williams
  Chezy-Mannings
Flow units (CFS, GPM, CMS and such)
  Select SI or US Customary – Preferably before building a model
  The program does not convert unit SYSTEMS

## Slide 10: Modeling protocol
Sketch a layout on paper
  Identify pipe diameters; length; roughness values
  Identify node elevations; demands
  Supply reservoir (or tank); identify reservoir pool elevation
  Identify pumps; pump curve in problem units
Start EPANET, and build the model

## Slide 11: Example 1
Example 1 – Flow between two reservoirs

## Slide 12: Example 2
Example 2 – Three reservoir (branched)

## Slide 13: Next Time
Additional Network models in EPANET