## Slide 1: CE 3372 Water Systems Design
Lesson 15: drainage hydrology – a review Fall 2020

## Slide 2: Outline
Hydrology
  Definitions and Motivation
  Hydrographs
  Design Storms

## Slide 3: Hydrology
“The science dealing with the occurrence, circulation, distribution, and properties of the waters of the earth and it’s atmosphere”
    -Dictionary.com
Notes: Studies the flow of water through and across surface
Hydrologic deals with rainfall while Hydraulic deals with flow of water in pipes

## Slide 4
Notes: “Hydrosphere”
Surface water + ground water

## Slide 5
Notes: Why is H&H engineering important??
Why do we care about runoff??
Safety. Reduce floods!
So whats the main purpose of H&H? Figuring out how to capture, store, and move the water into the ocean.
To do all of that requires calculations
HCFCD Mission: Provide flood damage reduction projects that work, with appropriate regard for community and natural values.

## Slide 6
Notes: That’s why basins are created.
Hint: those pretty “lakes” in neighborhoods and golf courses are actually detention basins.
Can you imagine what would happen if that basin was not designed properly and all those houses flooded?
So the focus is HOW do we accurately calculate rainfall runoff, HOW to capture and transport it, and HOW do we design storage spaces to hold all of the rainfall?

## Slide 7: Peak Flow/Discharge
Discharge [L3/T]- Volume of water through a given cross-sectional area at a period of time
Peak flow corresponds to maximum water levels reached during a rainfall event
Flood Timelapse
Notes: discharge is volume, at the peak discharge (the most volume of flow, it’s going to give you the max water levels and max volume you need to worry about for the storm) = width xdepthx velocity
Because the peak flow also corresponds to the maximum water level reached during the event, it is of interest in flood studies.
The stream rises to a peak flow after each precipitation event, then falls in a slow recession.

## Slide 8: Rainfall Frequency
Frequency (Return Period) and probability (AEP) are related
Frequency (years) = 100 / Probability (%)
Ex: 2-year =100 / 50%
Notes: Before estimating runoff, you need to choose a storm you’re designing for
*Exceedance Probability – storm has that chance of being equaled or exceeded
Potential harm vs> acceptable rish

## Slide 9: Hydrographs

## Slide 10: Hydrograph
Graph – Flow vs. Time
Notes: How discharge changes over time ( min, hours, years,decade etc.)
Can be used to derive runoff from any excess rainfall on the watershed.
Assumptions
  Excess rainfall has constant intensity during duration
  Excess rainfall is uniformly distributed on watershed

## Slide 11
Before
Rain
After
Rain &
water
moves
to streams

## Slide 12: Hydrographs
Permeable Low infiltration
Notes: Lag time is from the start of the rainfall to the PEAK discharge
Right ex: concrete urban areas

## Slide 15: Design intensities

## Slide 16: Precipitation
Intensity-Duration-Frequency
  NOAA Atlas 14
  EBDLKUP-2015 (Being replaced by a TAMU-TTI product)
Design Storms
  SCS Precip. Distributions
  TxHYETO-2015 (Being replaced by a TAMU-TTI product)

## Slide 17: Precipitation Variables
There are four variables of engineering interest:
  Intensity: how hard it rains
  Duration: how long it rains at any given intensity
  Frequency: how often it rains at any given intensity and duration
  Spatial Distribution: the equivalent uniform rainfall depth over an area

## Slide 18: Depth-Duration-Frequency
Depth of rainfall is the accumulated depth (in a gage) over some time interval.
Duration is that time interval.
Frequency is the probability (like AEP) of observing the depth over the given duration.

## Slide 19: Depth-Duration-Frequency
DDF curve
e.q. 12 hour, 100-year (AEP=1%), depth is 70 millimeters
Frequency
AEP; ARI
Duration
Depth

## Slide 20: Intensity
An alternate to DDF is to present the magnitude as an intensity (a rate).
Intensity is the ratio of an accumulated depth to some averaging time, usually the duration.
Intensity is NOT the instantaneous rainfall rate

## Slide 21: Intensity-Depth Relationship
Intensity (average rate) from depth
e.q. 12 hour, 100-year (AEP=1%), depth is 70 mm
average intensity is 70mm/12hr = 5.8 mm/hr
Duration
Depth
Notes: Intensity is related to depth and duration. The intensity is the ratio of depth to a particular duration. For example, if the duration or averaging time is 12 hours and the accumulated depth for 12 hours is 70 mm (about 3 inches), then the average rate is 70mm/12hours = 5.8 mm/hour. This average rate, if applied over 12 hours will produce the depth of 70mm.

## Slide 22: Intensity-Duration-Frequency
IDF curves
e.q. 20 min, 5-year (AEP=20%), intensity is 5.5 in/hr
Frequency
AEP; ARI
Intensity
Notes: The family of curves that depicts the relationship between the intensity, duration, and frequency of precipitation at a point is a fundamental part of the rational equation method for storm water drainage design.

## Slide 23: Estimating Depth and Intensity
DDF can be constructed from maps of depth for a given duration and AEP.
Such maps are available from:
  NWS TP40 (online) << Deprecated
  NWS HY35 (online) << Deprecated
  NOAA Atlas 14 (online)
  Texas DDF Atlas (online) << Deprecated
Other tools include:
  EBDLKUP-2015 << Deprecated

## Slide 24: DDF Maps (Direct Access)

## Slide 25: DDF Maps (Direct Access)

## Slide 26: DDF Maps (Direct Access)
The interface also has a link to the original document

## Slide 27: NOAA Atlas 14
A tool for use outside Texas is NOAA Atlas 14
  Texas is one of a few states not yet in the Atlas
The Atlas is an on-line tool that returns tables of depths for given geographic locations
The on-line tool is called the Precipitation Frequency Data Server
http://hdsc.nws.noaa.gov/hdsc/pfds/

## Slide 28: NOAA Atlas 14

## Slide 29: NOAA Atlas 14

## Slide 30: NOAA Atlas 14

## Slide 31: EBDLKUP-2015
EBDLKUP-2015 is a spreadsheet tool for Texas that produces intensity estimates by county for user supplied averaging times
The intensity estimates are based on the depths in the DDF Atlas
Suitable for Texas Only!
DEPRECATED SHOULD NOT USE -- USE NOAA ATLAS 14

## Slide 32: Depth, Intensity, and Duration
Conversion from Depth-Duration to Intensity-Duration is obtained by the ratio of depth to duration
Conversion from Intensity-Duration to Depth-Duration is obtained by multiplication
using same duration!

## Slide 33: Design hyetographs

## Slide 34: Hyetographs
The IDF approach only estimates average rate (over an averaging time)
When time behavior of a storm is important then we have to generate hyetographs (time series of rainfall)
Design storms are statistical models of such temporal behavior and are used in hydrologic models when hydrographs need to be generated

## Slide 35: Rainfall Distributions
Rainfall distributions represent temporal patterns of a storm.
A rainfall distribution is also called a hyetograph.
Rainfall distributions are used when we need to estimate an entire hydrograph.

## Slide 36: Rainfall Distributions
Each “block” represents the amount of rainfall for the time interval
The diagram is called “incremental” rainfall
The running sum of the blocks is the cumulative distribution

## Slide 37: Rainfall distributions
Distributions are created from historical storms and analyzed to generate statistical models of rainfall – these models are called design storms.
Design storm distributions are typically dimensionless hyetographs
  NRCS Type Storms (24 hour, 6 hour)
  Empirical Texas Hyetographs (TxHYETO-2015)

## Slide 38: SCS Rainfall Type Curves
SCS(1973) analyzed DDF curves to develop dimensionless rainfall temporal patterns called type curves for four different regions in the US.
SCS type curves are in the form of percentage mass (cumulative) curves based on 24-hr rainfall of the desired frequency.
Intended for use with the SCS Curve Number runoff generation model!

## Slide 39: SCS Rainfall Type Curves
Location selects the Type Curve
Module 8

## Slide 40: SCS Rainfall Type Curves
The 24-hour precipitation depth of desired frequency is specified (DDF Atlas), the SCS type curve is rescaled (multiplied by the known number) to get the time distribution.

## Slide 41: Rainfall distributions

## Slide 42: Rainfall distributions

## Slide 43: SCS Rainfall Type Curves
Using the Type Curves
Use DDF Atlas, TP-40, etc. to set total depth, P for the 24 hour storm (or 6 hour storm)
Pick appropriate SCS type curve (location).
Multiply (rescale) the type curve with P to get the design mass curve.
Get the incremental precipitation from the rescaled mass curve to develop the design hyetograph.

## Slide 44: Example: SCS Design Storm
Generate a design hyetograph for a 25-year, 24-hour duration SCS Type-III storm in Harris County using a one-hour time increments
  Look up 24-hour,25-year depth for Harris County in the DDF Atlas.
  Cumulative fraction - interpolate SCS table
  Cumulative rainfall = product of cumulative fraction * total 24-hour rainfall (10.01 in)
  Incremental rainfall = difference between current and preceding cumulative rainfall
  Plot results of incremental

## Slide 45: Example: Generate SCS Design Storm
Look up 24-hour,25-year depth for Harris County in the DDF Atlas.
P ~ 10 inches

## Slide 46: Example: SCS Design Storm
SCS Tabulation
DDF Atlas
Module 8

## Slide 47: Texas Empirical Hyetographs
Alternative to SCS Type Curves is the Texas Empirical Hyetographs
  Based on Texas data.
  Reflects “front loading” observed in many real storms.
  Rescales time and depth.

## Slide 48: Texas Empirical Hyetographs
Rescale Time
Rescale Depth
Average Intensity

## Slide 49: Texas Empirical Hyetographs
Use the 50th percentile curve (median storm).
  Multiply the time axis by the storm duration.
  Multiply the depth axis by the storm depth.
  Result is a design storm for given duration and AEP.

## Slide 50: Example: Texas Empirical Hyetographs
Construct a design storm for the 3-hour, 2-year rainfall in Harris County using the Texas Empirical Hyetograph
  Obtain the depth from the DDF Atlas
  Rescale the depth and time using the Texas Empirical Hyetograph
Module 8

## Slide 51: Example: Texas Empirical Hyetographs
0 hours
2.6 inches
1.3 inches
3 hours
1 hours
2 hours

## Slide 52: Example: Texas Empirical Hyetographs
Probably easier to use the tabulation
SIR-2004-5075
Chart: Time (hours)
| 0.0 | 0.0750000000000001 | 0.15 | 0.225 | 0.3 | 0.375000000000001 | 0.45 | 0.525 | 0.600000000000001 | 0.675000000000002 | 0.750000000000001 | 0.825000000000001 | 0.9 | 0.975000000000001 | 1.05 | 1.125 | 1.2 | 1.274999999999997 | 1.35 | 1.424999999999997 | 1.5 | 1.575 | 1.65 | 1.724999999999999 | 1.8 | 1.875 | 1.950000000000001 | 2.025 | 2.1 | 2.175 | 2.25 | 2.325 | 2.4 | 2.474999999999999 | 2.55 | 2.625 | 2.7 | 2.775 | 2.849999999999999 | 2.925 | 3.0
Elapsed Time | 0 | 0.16562 | 0.35308 | 0.53274 | 0.69758 | 0.84292 | 0.96746 | 1.066 | 1.1469 | 1.2103 | 1.262 | 1.306 | 1.3437 | 1.3754 | 1.411 | 1.4427 | 1.4768 | 1.5088 | 1.5421 | 1.5727 | 1.6112 | 1.6513 | 1.7001 | 1.7566 | 1.8161 | 1.8749 | 1.9323 | 1.9859 | 2.0335 | 2.08 | 2.1219 | 2.1645 | 2.2058 | 2.25 | 2.2958 | 2.3455 | 2.3967 | 2.4497 | 2.5015 | 2.5535 | 2.6

## Slide 53: TxHYETO-2015
Texas Empirical Hyetograph tool that approximates the hyetographs using a function fit.
User supplies:
  Depth
  Duration
  Desired Time Steps (increments)
Tool returns a time series of cumulative depth every increment (intended for copy-paste into HEC-HMS)

## Slide 54: Hydrologic Analysis
Runoff models:
  Rational Method
  HCFCD Discharge-Area Curves (1960s)
  TxDOT and USGS Regression Equations
  SCS CN MODEL
Infiltration models
  GREEN-AMPT
  HORTON
Notes: So how do we calc peak flow and volumes?
A comparison of the various methodologies shows a wide variation in computed peak discharges for similar watershed and channel conditions. On occasion, these variations lead to confusion and inconsistency among the engineering community
So diff people have diff standards. Which to pick!? It’s like a checklist
Methodology depends primarily on the drainage area of the project. In some cases, the complexity of the design or level of accuracy may influence the method selected.

## Slide 55: Hydrologic Analysis
Unit hydrograph models
  Clark Unit Hydrograph
  Soil Conservation Service (SCS) Unit Hydrograph Method
  Johnson & Sayre Curves and Generalized Regression Equations
  Gamma uh (Asquith)
Notes: So how do we calc peak flow and volumes?
A comparison of the various methodologies shows a wide variation in computed peak discharges for similar watershed and channel conditions. On occasion, these variations lead to confusion and inconsistency among the engineering community
So diff people have diff standards. Which to pick!? It’s like a checklist
Methodology depends primarily on the drainage area of the project. In some cases, the complexity of the design or level of accuracy may influence the method selected.

## Slide 56
Notes: iSWM Criteria Manual used in Dallas outlines which method you can use for which

## Slide 57
Notes: TxDOT’s limitations are limited to watersheds 200 acres or smaller for Rational. So it varies

## Slide 58: Peak discharge

## Slide 59: Rational Method
Qp = CiA
  where
  QP= peak runoff [L3/T]
C = a dimensionless coefficient
i = rainfall intensity [L/T]
A = drainage area [L2]
Notes: Done for VERY small areas. Don’t need to create a hydrograph
TxDOTs main formula
method provides the designer with a peak discharge value, but does not provide a time series of flow nor flow volume.

## Slide 60: Rational Method - C

## Slide 61: Rational Method - i
Qp = CiA
Rainfall intensity (I) = total amount of rain (rainfall depth) falling over a given time of concentration [L/T]
Notes: Explain the depth on the board.

## Slide 62: Rational Method - i
Pd = depth of rainfall (in. or mm) for AEP design storm of duration
tc = drainage area time of concentration (hr.)
Notes: Explain the depth on the board.

## Slide 63: Depth-Duration Frequency
United States Geological Service Report (USGS), Asquith (1988)
Notes: Instead of having to research different depths for different storms, it’s been done by USGS through DDF maps

## Slide 64: IDF Curves
Notes: IDF Curves

## Slide 65: Rational Method - i
Notes: There are different EBD values JUST for texas. On a spreadsheet called EBDLKUP

## Slide 66: Time of Concentration (Tc)
Time required (after start of rainfall event) for most distant point in watershed to begin contributing runoff to the watershed outlet
Typical is 10min to 300min; most jurisdictions restrict the small end to 10 (or 5 minutes)
Notes: “In the context of the rational method then, tc represents the time at which all areas of the watershed that will contribute runoff are just contributing runoff to the outlet. That is, at tc, the watershed is fully contributing. We choose to use this time to select the rainfall intensity for application of the rational method.
If the chosen storm duration is larger than tc, then the rainfall intensity will be less than that at tc. Therefore, the peak discharge estimated using the rational method will be less than the optimal value. If the chosen storm duration is less than tc, then the watershed is not fully contributing runoff to the outlet for that storm length, and the optimal value will not be realized. Therefore, we choose the storm length to be equal to tc for use in estimating peak discharges using the rational method.
All methods for estimating tc are empirical, that is, each is based on the analysis of one or more datasets. The methods are not, in general, based on theoretical fluid mechanics. “
-Dr Thompson
Just like I theres multiple ways to calc Tc

## Slide 67: Kerby-Kirpich Method
Applicable to watersheds
  area: 0.25 sq. mi. to 150 sq. mi.
  main channel slopes: 0.002 to 0.02 (ft/ft)
  main channel lengths: 1 to 50 miles
  (Roussel et al. 2005)

## Slide 70: NRCS Method
Applicable for:
  small watersheds
  majority overland flow
  (so timing of the peak flow is not significantly affected by the contribution flow routed through underground storm drain systems.)
Notes: National Resources Conservation Services

## Slide 74: NRCS Upland Method
Specify flow path
Determine cover on flow path
Determine slope(s) along path
  Partition into different cover types and slopes along path
Apply velocity model on each part add times for entire path

## Slide 75: Upland Method Velocity Chart

## Slide 76: Watershed Length
Notes: The watershed length (L) is
 the length of the longest watercourse for the subbasin.
 defined from the subbasin outflow point to the upstream subbasin
watershed boundary.
 measured along the longest definable channel and overland runoff
path, often following roadside ditches and major streets.
So if it was a small development it’s the longest flow path around houses etc.

## Slide 77: Watershed Slope

## Slide 78: Rational Method
Qp = CiA
Find tc to calculate intensity
Plug and chug

## Slide 79: HCFCD Site Runoff Curves
Notes: Alt method to calculating Peak Flow. HCFCD uses Site Runoff Curves.
Used for less than 640 acres

## Slide 80: Regression Equations
Notes: These are all TEXAS concepts. If you leave the state to do engineering you can’t apply these equations.

## Slide 81: Texas Regression Eq.
Regression equations are used to transfer flood characteristics from gauged to ungauged sites
  Done by using watershed and climatic characteristics as explanatory or predictor variables
Reliable > 10 sq. mi. drainage area
Only for non-urbanized watersheds
Other states have their OWN (Different) equations!
Notes: Regression equations are recommended as the primary hydrologic method for off-system (non-TxDOT) projectsfor on-system projects, they are recommended as a check on other methods. Omega EM regression equations are reliable beyond 10 sq. mi. drainage area.
Regression equations are used to transfer flood characteristics from gauged to ungauged sites through the use of watershed and climatic characteristics as explanatory or predictor variables. USGS has developed such regression equations for natural basins throughout the State of Texas.

## Slide 82: Texas Regression Eq.

## Slide 83
Notes: RSE, residual standard error in log10-units of cubic feet per second;
PRESS, Prediction Error Sum of Squares;

## Slide 85
Notes: Equations have been developed for natural basins in 1-degree latitude and longitude quadrangles in Texas.
The approach used to develop the regional equations is referred to as the “Regression Equations for Estimation of Annual Peak-Streamflow Frequency for Undeveloped Watersheds in Texas Using an L-moment-Based, PRESS-Minimized, Residual-Adjusted Approach.”
For development and use of regression equations a natural basin is defined as having less than 10 percent impervious cover, less than 10 percent of its drainage area controlled by reservoirs, and no other human-related factors affecting streamflow (USGS 2001). The equations are therefore not applicable to urban watersheds.

## Slide 86: Value of Regression Equations
The regression equations are not really intended for hydraulic structure design – but:
  They are useful to check that other methods are about the correct magnitude

## Slide 87: NRCS Curve Number
One step up from Rational in complexity is the CN method
CN model is built-in to SWMM
  Rational Method is not built-in, but a hack is presented later in the course.

## Slide 88: Infiltration Models
One step up from Curve Number is an infiltration model.
  Green-Ampt is quite commonly used.
    GA model is built-in to SWMM
  Hortonian Infiltration is also used.
    Horton is built-in to SWMM

## Slide 89: Example of Using Rational Equation
Estimate the peak discharge from a 200 acre, undeveloped, sandy-loam drainage area with 3-5% slope in Bexar County.
The desired AEP is 0.5 (50%).
The time of concentration is 60 minutes.

## Slide 90: Required Information
Depth for 60-minute, 50% Chance storm in Bexar County, Texas.
Tc for a 200 acre parcel Given – if not would need a map and apply:
    Kerby-Kirpich; NRCS Upland; or NRCS Velocity
Runoff coefficient for the parcel

## Slide 91: Depth for 60-minute, 50% Chance storm in Bexar County, Texas.
DDF Atlas or EBDLKUP-2015 NOAA Atlas 14

## Slide 92: Intensity to be Applied
Tc = 60 minutes
D = 1.83 inches
Intensity = 1.83 inches/hour

## Slide 93: Runoff Coefficient
Look up in Table
  C=0.25

## Slide 94: Compute Qp
Apply equation:
Qp = C i A = (0.25)(1.83 in/hr)(200 acres) = 91.5 cfs
Pay attention to units, in SI the equation has a unit conversion constant!

## Slide 95: Practical Considerations
The designer will need to consider topography and flow paths to
    Estimate Tc using some defensible method
Use locally relevant depth-duration-frequency tools
    EBDLKUP, DDF Atlas for Texas
    NOAA for elsewhere
Use meaningful runoff coefficients
Be sure applying appropriately

## Slide 96: NEXT TIME
Inlets
  Inlets to capture the runoff from a sub-catchment
  Hydraulics consideration for:
    Curb-on-grade
    Curb-in-sag
    Drop inlets