## Slide 1: CE 3372 Water Systems Design
Lesson 20: design storms on small sub-catchments

## Slide 2: Outline
Hydrology
  Design Storms (Review)
  Application to Tanglewilde Example

## Slide 3: Design hyetographs
Also called design storms

## Slide 4: Hyetographs
The IDF approach only estimates average rate (over an averaging time)
When time behavior of a storm is important then we have to generate hyetographs (time series of rainfall)
Design storms are statistical models of such temporal behavior and are used in hydrologic models when hydrographs need to be generated

## Slide 5: Rainfall Distributions
Each “block” represents the amount of rainfall for the time interval
The diagram is called “incremental” rainfall
The running sum of the blocks is the cumulative distribution

## Slide 6: Rainfall distributions
Distributions are created from historical storms and analyzed to generate statistical models of rainfall – these models are called design storms.
Design storm distributions are typically dimensionless hyetographs
  NRCS Type Storms (24 hour, 6 hour)
  Triangular Hyetograph Method
  Empirical Texas Hyetographs (TxHYETO-2015)
  Alternating Block Method
  Instantaneous Intensity Method

## Slide 7: SCS Rainfall Type Curves
SCS(1973) analyzed DDF curves to develop dimensionless rainfall temporal patterns called type curves for four different regions in the US.
SCS type curves are in the form of percentage mass (cumulative) curves based on 24-hr rainfall of the desired frequency.
Intended for use with the SCS Curve Number runoff generation model!

## Slide 8: SCS Rainfall Type Curves
Location selects the Type Curve
Module 8

## Slide 9: SCS Rainfall Type Curves
The 24-hour precipitation depth of desired frequency is specified (DDF Atlas), the SCS type curve is rescaled (multiplied by the known number) to get the time distribution.

## Slide 10: Rainfall distributions

## Slide 11: Rainfall distributions

## Slide 12: SCS Rainfall Type Curves
Using the Type Curves
Use NOAA Atlas 14 DDF Atlas, TP-40, etc. to set total depth, P for the 24 hour storm (or 6 hour storm)
Pick appropriate SCS type curve (location).
Multiply (rescale) the type curve with P to get the design mass curve.
Get the incremental precipitation from the rescaled mass curve to develop the design hyetograph.

## Slide 13: Example: SCS Design Storm
Generate a design hyetograph for a 25-year, 24-hour duration SCS Type-III storm in Harris County using a one-hour time increments
  Look up 24-hour,25-year depth for Harris County in the NOAA Atlas 14, Vol. 11. DDF Atlas.
  Cumulative fraction - interpolate SCS table
  Cumulative rainfall = product of cumulative fraction * total 24-hour rainfall (10.01 in)
  Incremental rainfall = difference between current and preceding cumulative rainfall
  Plot results of incremental

## Slide 14: This slide is deprecated
Look up 24-hour,25-year depth for Harris County in the DDF Atlas.
P ~ 10 inches

## Slide 15: SCS DESIGN STORM
Look up 24-hour,25-year depth for Harris County in the DDF Atlas.
P ~ 11.7 inches

## Slide 16: This slide is deprecated
SCS Tabulation
DDF Atlas
Module 8

## Slide 17: Example: SCS Design Storm
SCS Tabulation
NOAA Atlas 14, Vol. 11 DDF Atlas

## Slide 18: Triangular hyetograph method
Determine advancement coefficient
Time to peak
Total Time

## Slide 19: Triangular hyetograph method
Texas-specific

## Slide 20: Texas Empirical Hyetographs
Alternative to SCS Type Curves is the Texas Empirical Hyetographs
  Based on Texas data.
  Reflects “front loading” observed in many real storms.
  Rescales time and depth.

## Slide 21: Texas Empirical Hyetographs
Rescale Time
Rescale Depth
Average Intensity

## Slide 22: Texas Empirical Hyetographs
Use the 50th percentile curve (median storm).
  Multiply the time axis by the storm duration.
  Multiply the depth axis by the storm depth.
  Result is a design storm for given duration and AEP.

## Slide 23: Example: Texas Empirical Hyetographs
Construct a design storm for the 3-hour, 2-year rainfall in Harris County using the Texas Empirical Hyetograph
  Obtain the depth from the DDF Atlas
  Rescale the depth and time using the Texas Empirical Hyetograph
Module 8

## Slide 24: Example: Texas Empirical Hyetographs
0 hours
2.6 inches
1.3 inches
3 hours
1 hours
2 hours

## Slide 25: Example: Texas Empirical Hyetographs
Probably easier to use the tabulation
SIR-2004-5075
Chart: Time (hours)
| 0 | 7.5000000000000094E-2 | 0.15 | 0.22500000000000001 | 0.3 | 0.375000000000001 | 0.45 | 0.52500000000000002 | 0.60000000000000098 | 0.67500000000000204 | 0.750000000000001 | 0.82500000000000095 | 0.9 | 0.97500000000000098 | 1.05 | 1.125 | 1.2 | 1.274999999999997 | 1.35 | 1.4249999999999969 | 1.5 | 1.575 | 1.65 | 1.724999999999999 | 1.8 | 1.875 | 1.9500000000000011 | 2.0249999999999999 | 2.1 | 2.1749999999999998 | 2.25 | 2.3250000000000002 | 2.4 | 2.4749999999999992 | 2.5499999999999998 | 2.625 | 2.7 | 2.7749999999999999 | 2.8499999999999992 | 2.9249999999999998 | 3
Elapsed Time | 0 | 0.16562 | 0.35308 | 0.53274 | 0.69758 | 0.84292 | 0.96746 | 1.066 | 1.1469 | 1.2103 | 1.262 | 1.306 | 1.3437 | 1.3754 | 1.411 | 1.4427 | 1.4768 | 1.5088 | 1.5421 | 1.5727 | 1.6112 | 1.6513 | 1.7001 | 1.7566 | 1.8161 | 1.8749 | 1.9323 | 1.9859 | 2.0335 | 2.08 | 2.1219 | 2.1645 | 2.2058 | 2.25 | 2.2958 | 2.3455 | 2.3967 | 2.4497 | 2.5015 | 2.5535 | 2.6

## Slide 26: TxHYETO-2015
Texas Empirical Hyetograph tool that approximates the hyetographs using a function fit.
User supplies:
  Depth
  Duration
  Desired Time Steps (increments)
Tool returns a time series of cumulative depth every increment (intended for copy-paste into HEC-HMS)

## Slide 27: Application of design storm for tanglewilde
Using the Tanglewilde problem as an example

## Slide 28: Application of design storm for tanglewilde
Using the Tanglewilde problem as an example
Does not specify storm type, so for completeness we will build using
  SCS 6-hour
  TXHYETO 6-hour

## Slide 29: Application of design storm for tanglewilde
Using the Tanglewilde problem as an example
Does not specify storm type, so for completeness we will build using
  SCS 6-hour
  TXHYETO 6-hour
NOAA Atlas 14, Vol 11. 6-hour, 5-year depth is 4.97 inches

## Slide 30: Application of design storm for tanglewilde
Using the Tanglewilde problem as an example
Does not specify storm type, so for completeness we will build using
  SCS 6-hour
  TXHYETO 6-hour
NOAA Atlas 14, Vol 11. 6-hour, 5-year depth is 4.97 inches
  Use interpolation to get onto uniform time intervals

## Slide 31: Application of design storm for tanglewilde
Using the Tanglewilde problem as an example
Does not specify storm type, so for completeness we will build using
  SCS 6-hour
  TXHYETO 6-hour
NOAA Atlas 14, Vol 11. 6-hour, 5-year depth is 4.97 inches
  Use interpolation to get onto uniform time intervals

## Slide 32: Application of design storm for tanglewilde
Using the Tanglewilde problem as an example
Does not specify storm type, so for completeness we will build using
  SCS 6-hour
  TXHYETO 6-hour
NOAA Atlas 14, Vol 11. 6-hour, 5-year depth is 4.97 inches
  Using TXHYETO-2015, no interpolation needed