## Slide 1: CE 3372 Water Systems Design
Lesson 17: Storm sewers Conduit design (size selection) by rational equation method Fall 2020

## Slide 2: Purposes
Conduits convey Flow from one location to another
  Pipes
  Culverts
  Open channels

## Slide 3: Conduit design
Select size, material, and slope
  Storm sewer – usually desire to operate with free surface (as an open channel)
  Sanitary sewer – similar usually want a free surface
  Size (diameter) is dictated by
    Flow required
    Burial depth relative to drop available

## Slide 4: methods
A good preliminary design can be obtained using a combination of the rational equation and manning’s equation
  Done without regard to downstream boundary conditions
  Needs to be checked using a hydraulic model (like SWMM)

## Slide 5: Preliminary design
Determine discharge in each pipe.
Size using manning’s equation (… in us customary)
Assumes full, but pipes will have free surface

## Slide 6: Preliminary design
Layout of system
  Drainage area and Inlets
  Pipes
  Outfall
  elevations

## Slide 7: Preliminary design
Drainage areas and inlets
  Determine inlet time of concentration
  Determine drainage area runoff coefficient

## Slide 8: Preliminary design
Pipes (Start upstream)
  Select pipe size
    Design guidelines
    Discharge criteria
    Velocity criteria
  Determine pipe travel time
From criterion
Adjust
Notes: 𝑉=1.49/𝑛 〖(𝐷/4)〗^(2/3) √𝑆

## Slide 9: Preliminary design
  At most upstream inlet
    Compute QP=CiA to the inlet from inlet time
    Size pipe from this inlet to hold QP
    ADD pipe travel time to inlet time
    Move to next node
Notes: 𝑉=1.49/𝑛 〖(𝐷/4)〗^(2/3) √𝑆

## Slide 10: Preliminary design
  At NEXT upstream inlet
    Compute QP=CiA to the inlet from inlet time
    Size pipe from this inlet to hold QP
    ADD pipe travel time to inlet time
    Move to next node
Notes: 𝑉=1.49/𝑛 〖(𝐷/4)〗^(2/3) √𝑆

## Slide 11: Preliminary design
  AT JUNCTION AND INLET
    Choose largest of:
    Local inlet time
    Upstream node+travel time
  Compute Qp LEAVING THE JUNCTION FROM:
  SIZE next pipe from this qp
local
Notes: 𝑉=1.49/𝑛 〖(𝐷/4)〗^(2/3) √𝑆

## Slide 12: Preliminary design
  Continue downstream in same fashion (from upstream to junction) until reach outlet
  Accumulate CA values and Tc as move downstream
  Checks include that all areas add up to total area
  Tc should be increasing in value as move downstream
local
Notes: 𝑉=1.49/𝑛 〖(𝐷/4)〗^(2/3) √𝑆

## Slide 13: Preliminary design
At outlet should have:
  Pipe sizes
  Pipe discharges
Next check hydraulics
  SWMM – enter QINLET directly and check pipe hydraulics
  SWMM – Approximate rational in SWMM to check a design hyetograph
  Use SWMM results to adjust design and produce a HGL drawing
local
Notes: 𝑉=1.49/𝑛 〖(𝐷/4)〗^(2/3) √𝑆

## Slide 14: Design storm sewer for Goodwin street
“Rational Method Storm Sewer Design” in Mays, L. W. (2008) Water Resources Engineering. Pearson-Prentice Hall (pp. 613-635)
Method: Rational Equation Design Method to make initial design for subsequent hydraulics analysis

## Slide 15: Preparation steps
Identify the individual drainage areas.
Determine the area of each contributing area, in acres. (ENGAUGE, PLANIMETER, etc)
Determine the rational runoff coefficient for each area (TABLE LOOKUP)

## Slide 16: DRAINAGE AREA 1.1
Identify the individual drainage areas.

## Slide 17: DRAINAGE AREA 1.2
Identify the individual drainage areas.

## Slide 18: DRAINAGE AREA 2.1
Identify the individual drainage areas.

## Slide 19: DRAINAGE AREA 2.2
Identify the individual drainage areas.

## Slide 20: DRAINAGE AREA 3.1
Identify the individual drainage areas.

## Slide 21: DRAINAGE AREA 3.2
Identify the individual drainage areas.

## Slide 22: DRAINAGE AREA 3.3
Identify the individual drainage areas.

## Slide 23: DRAINAGE AREA 4.1
Identify the individual drainage areas.

## Slide 24: DRAINAGE AREA 4.2
Identify the individual drainage areas.

## Slide 25: DRAINAGE AREA 5.1
Identify the individual drainage areas.

## Slide 26: DRAINAGE AREA 5.2
Identify the individual drainage areas.

## Slide 27: DRAINAGE AREA 5.3
Identify the individual drainage areas.

## Slide 28: DRAINAGE AREA 6.1
Identify the individual drainage areas.

## Slide 29: DRAINAGE AREA 7.1
Identify the individual drainage areas.

## Slide 30: Calibrate area measurement tool
Measure areas using appropriate tools
  E.g. Acrobat Pro
    Need to measure a known area
    Save the conversion factor
Area =400X400/43560 = 3.67 acres
A = 3.67 acres

## Slide 31: Calibrate area measurement tool
Measure areas using Acrobat Pro
  Activate the measurement toolkit
  Select Area
  Measure the orange rectangle
  Save the conversion factor: 2.43 sq.in. == 3.67 acres
A = 3.67 acres

## Slide 32: DRAINAGE AREA 1.1
Identify the individual drainage areas.
Determine the area of each contributing area, in acres. (G3DATA; PLANIMETER, etc)
Area = 1.50*3.67/2.43 = 2.26 acres
A = 3.67 acres

## Slide 33: DRAINAGE AREA 1.2
Identify the individual drainage areas.
Determine the area of each contributing area, in acres. (ENGAUGE, PLANIMETER, etc)
Area = 0.84*3.67/2.43 = 1.26 acres
A = 3.67 acres

## Slide 34: DRAINAGE AREA 2.1
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 2.58*3.67/2.43 = 3.89 acres
A = 3.67 acres

## Slide 35: DRAINAGE AREA 2.2
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 0.35*3.67/2.43 = 0.53 acres
A = 3.67 acres

## Slide 36: DRAINAGE AREA 3.1
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 0.45*3.67/2.43 = 0.68 acres
A = 3.67 acres

## Slide 37: DRAINAGE AREA 3.2
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 0.30*3.67/2.43 = 0.45 acres
A = 3.67 acres

## Slide 38: DRAINAGE AREA 3.3
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 1.05*3.67/2.43 = 1.58 acres
A = 3.67 acres

## Slide 39: DRAINAGE AREA 4.1
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 1.33*3.67/2.43 = 2.01 acres
A = 3.67 acres

## Slide 40: DRAINAGE AREA 4.2
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 0.44*3.67/2.43 = 0.66 acres
A = 3.67 acres

## Slide 41: DRAINAGE AREA 5.1
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 0.78*3.67/2.43 = 1.17 acres
A = 3.67 acres

## Slide 42: DRAINAGE AREA 5.2
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 0.44*3.67/2.43 = 0.66 acres
A = 3.67 acres

## Slide 43: DRAINAGE AREA 5.3
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 1.16*3.67/2.43 = 1.75 acres
A = 3.67 acres

## Slide 44: DRAINAGE AREA 6.1
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 0.36*3.67/2.43 = 0.54 acres
A = 3.67 acres

## Slide 45: DRAINAGE AREA 7.1
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 1.44*3.67/2.43 = 2.17 acres
A = 3.67 acres

## Slide 46: Estimate runoff coefficients
For each area estimate a runoff coefficient
Usually based on a table lookup and surface description

## Slide 47: DRAINAGE AREA 1.1
Identify the individual drainage areas.
Determine the area of each contributing area, in acres. (ENGAUGE, PLANIMETER, etc)
Area = 1.50*3.67/2.43 = 2.26 acres
C = 0.65
A = 3.67 acres

## Slide 48: DRAINAGE AREA 1.2
Identify the individual drainage areas.
Determine the area of each contributing area, in acres. (ENGAUGE, PLANIMETER, etc)
Area = 0.84*3.67/2.43 = 1.26 acres
C = 0.80
A = 3.67 acres

## Slide 49: DRAINAGE AREA 2.1
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 2.58*3.67/2.43 = 3.89 acres
C= 0.70
A = 3.67 acres

## Slide 50: DRAINAGE AREA 2.2
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 0.35*3.67/2.43 = 0.53 acres
C = 0.80
A = 3.67 acres

## Slide 51: DRAINAGE AREA 3.1
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 0.45*3.67/2.43 = 0.68 acres
C = 0.70
A = 3.67 acres

## Slide 52: DRAINAGE AREA 3.2
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 0.30*3.67/2.43 = 0.45 acres
C = 0.85
A = 3.67 acres

## Slide 53: DRAINAGE AREA 3.3
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 1.05*3.67/2.43 = 1.58 acres
C = 0.65
A = 3.67 acres

## Slide 54: DRAINAGE AREA 4.1
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 1.33*3.67/2.43 = 2.01 acres
C = 0.75
A = 3.67 acres

## Slide 55: DRAINAGE AREA 4.2
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 0.44*3.67/2.43 = 0.66 acres
C = 0.85
A = 3.67 acres

## Slide 56: DRAINAGE AREA 5.1
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 0.78*3.67/2.43 = 1.17 acres
C = 0.70
A = 3.67 acres

## Slide 57: DRAINAGE AREA 5.2
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 0.44*3.67/2.43 = 0.66 acres
C = 0.65
A = 3.67 acres

## Slide 58: DRAINAGE AREA 5.3
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 1.16*3.67/2.43 = 1.75 acres
C = 0.55
A = 3.67 acres

## Slide 59: DRAINAGE AREA 6.1
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 0.36*3.67/2.43 = 0.54 acres
C = 0.75
A = 3.67 acres

## Slide 60: DRAINAGE AREA 7.1
Identify the individual drainage areas.
Determine the area of each contributing area, in acres.
Area = 1.44*3.67/2.43 = 2.17 acres
C = 0.70
A = 3.67 acres

## Slide 61: IDENTIFY AND MEASURE CONDUIT LENGTHS
Use ACROBAT to measure distances between Node ID
Select distance tool
Measure the 400 foot scale
Save scale factor 1.51 in == 400 feet

## Slide 62: PIPE 1.1
Connects 1.1 to 2.1
Length = 1.57*400/1.51 = 415 ft
Repeat for all the other pipes

## Slide 63: Gather the information into a spreadsheet
Build a sheet with the information
Note the naming convention (a bit awkward, but faithful to the original example)

## Slide 64: Determine inlet times for each drainage area
Measure actual best-guess flow path
  Find Slope (737.5 – 732.3)/(0.92*400/1.51) = 5.2ft/243.7 ft = 0.021 (2.1%)
  Determine some kind of cover
  Apply NRCS Velocity, NRCS Upland, or Kerby-Kirpich
  Use method that makes most sense

## Slide 65: Determine inlet times for each drainage area
NRCS Upland Method
Measure actual best-guess flow path
  Path = 243.7 ft
  Slope = 0.021 (2.1%)
Inlet Time ~ 11 minutes
Repeat for each drainage area, populate spreadsheet

## Slide 66: Determine inlet times for each drainage area
Repeat for each drainage area, populate spreadsheet

## Slide 67: Estimate pipe slopes
Use the node elevations and topographic map to estimate pipe slopes
Contour lines
Elevation Markers

## Slide 68: Estimate pipe slopes
Use the node elevations and topographic map to estimate pipe slopes
Populate the spreadsheet

## Slide 69: Intensity equation
Next we will need to precipitation information for the design.
Easiest for this example is to build an IDF curve for the location.
The basin in the example is in Urbana, Illinois – Use NOAA Atlas 14
For the example use a 2-yr ARI

## Slide 70: Intensity equation
Download the table
Use the 2-nd column

## Slide 71: Intensity equation
Download the table
Use the 2-nd column
Use solver to fit
Use this equation for estimating intensity and runoff

## Slide 72: Intensity equation
Intensity function for the example:
This can be coded into an analysis spreadsheet directly

## Slide 73: Begin with most upstream node
Intensity Equation
Rational Method
Discharge to Inlet