## Slide 1: CE 3372 Water Systems Design
Lesson 19: STORM SEWER DESIGN EXAMPLE (Goodwin street STORM SEWER) And SWMM Hydrology Fall 2020

## Slide 2: Goodwin street example (Continued)
Build network in SWMM using our initial design by rational method from previous lesson.

## Slide 3: SWMM as Hydrologic Model
Sub-catchments
  Infiltration model (runoff generation)
Raingages
  Time-series of rainfall (hyetograph)

## Slide 4: SWMM as Hydrologic Model
500 ft
2.5 acres
4.0 acres
250 ft
475 ft
S0=0.01
S0=0.01
40% Impervious
15% impervious
30 ft
Size pipes so that velocity is 3-7 ft/sec
Slope no greater than 0.01
700 ft

## Slide 5: SWMM as Hydrologic Model
Load the picture into SWMM

## Slide 6: SWMM as Hydrologic Model
3 Nodes + Outfall

## Slide 7: SWMM as Hydrologic Model
Invert elevations
  (example, these would be design values, except for outfall, adjust to get velocity)
    Outfall = 0
    Node 3 = 700*(0.01)=7 ft
      Offset of 2 ft
    Node 2 = 7+2+0.01(30) = 9.3
    Node 1 = 7+2+0.01(500) = 14

## Slide 8: SWMM as Hydrologic Model
3 Pipes, 24” diameter, concrete (n=0.013)

## Slide 9: SWMM as Hydrologic Model
2 sub-catchments

## Slide 10: SWMM as Hydrologic Model
Choose a Runoff Generation Mechanism!
  For this scale Rational is logical, but not part of SWMM – need a hack!

## Slide 11: Hacking Rational Method in SWMM
Runoff Generation
  No explicit rational method for runoff generation
  Horton, Green-Ampt, and CN.

## Slide 12: Hacking Rational Method in SWMM
Suppose we want to simulate a 10.9 acre drainage area, with Tc =49 minutes, and C=0.32 and applied rain depth is 0.87 inches.
  I = 0.87inches/49min X 60 min/hr = 1.06 in/hr
  Qp = (0.32)(1.06)(10.9) = 3.7 cfs
Notes: No need for SWMM to compute Qp, unless we need to study hydraulics later!
Here’s how. Build an equibvalent SWMM model

## Slide 13: Hacking Rational Method in SWMM
Equivalent SWMM model:
  Raingage
  Catchment
  Outlet
Notes: No need for SWMM to compute Qp, unless we need to study hydraulics later!
Here’s how. Build an equibvalent SWMM model

## Slide 14: Hacking a Rational Method in SWMM
Equivalent SWMM model:
  Raingage  Constant intensity of 1.06 in.hr
  Catchment  Area = 10.9 acres
  Outlet
Notes: No need for SWMM to compute Qp, unless we need to study hydraulics later!
Here’s how. Build an equibvalent SWMM model

## Slide 15: Hacking a Rational Method in SWMM
Raingage  Constant intensity of 1.06 in/hr
Notes: No need for SWMM to compute Qp, unless we need to study hydraulics later!
Here’s how. Build an equibvalent SWMM model

## Slide 16: Hacking Rational Method in SWMM
Catchment  Set size, set to 100% impervious
  Run to adjust width & slope
    Arrival time of Qp at 50 minutes
    Qp = 11.65 cfs (C=1)
Notes: No need for SWMM to compute Qp, unless we need to study hydraulics later!
Here’s how. Build an equibvalent SWMM model

## Slide 17: Hacking a Rational Method in SWMM
Catchment  Set size, set to 100% impervious
  Width = 1500
    Arrival time of Qp at 50 minutes
    Qp = 11.65 cfs (C=1)
Notes: No need for SWMM to compute Qp, unless we need to study hydraulics later!
Here’s how. Build an equibvalent SWMM model

## Slide 18: Hacking a Rational Method in SWMM
Catchment  Adjust
  Infiltration rates to be large
  Set %impervious = runoff coefficient, C
Max and Min > 1.06 in/hr
Ensures all rain on pervious will infiltrate
Correct Qp
May want to adjust width once more to get timing about right – Just hacked Q=CiA into SWMM!
Notes: No need for SWMM to compute Qp, unless we need to study hydraulics later!
Here’s how. Build an equibvalent SWMM model

## Slide 19: SWMM as Hydrologic Model
Suppress background, check layout

## Slide 20: SWMM as Hydrologic Model
Insert a raingage

## Slide 21: SWMM as Hydrologic Model
Apply the raingage to the sub-catcments

## Slide 22: SWMM as Hydrologic Model
Set the time window, and run the model

## Slide 23: SWMM as Hydrologic Model
For larger scale (lots of small catchments) there will be a desire to use SCS storms or even historical events to evaluate the design.
The next example illustrates how to use HEC-HMS as a tool to generate rainfall for use in SWMM.

## Slide 24: SWMM as Hydrologic Model

## Slide 25: SWMM as Hydrologic Model
Assign a storm to a raingage
  Suppose instructed to use SCS-Type II storm and parameterize for San Antonio, Texas
  SCS Storms are built-in to HEC-HMS, so take advantage of that to generate a rainfall time series for SWMM

## Slide 26: SWMM as Hydrologic Model
How to generate SCS Type storms
  Select Annual Exceedance Probability (AEP) or Annual Recurrence Interval (ARI)
  Look up 24 hour depth for the ARI and location
  Generate 24 hour storm using SCS tabulations or HEC-HMS
  Put the time series into SWMM and run the hydraulics

## Slide 27: SWMM as Hydrologic Model
How to generate SCS Type storms
  Select Annual Exceedance Probability (AEP) or Annual Recurrence Interval (ARI)
    Given in the project statement, a 10% chance AEP or 10-year ARI (same probability) is specified.

## Slide 28: SWMM as Hydrologic Model
How to generate SCS Type storms
  Look up 24 hour storm depth for the AEP/ARI and location

## Slide 30: SWMM as Hydrologic Model
How to generate SCS Type storms
  Select Annual Exceedance Probability (AEP) or Annual Recurrence Interval (ARI)
  Look up 24 hour depth for the ARI and location
    6 inches for Bexar County, TX

## Slide 31: SWMM as Hydrologic Model
How to generate SCS Type storms
  Generate 24 hour storm using SCS tabulations or HEC-HMS
    Get the SWMM model built
    Open HMS and generate a SCS storm from the meterological model

## Slide 32: Build a Minimal HEC Model

## Slide 33: Build a Minimal HEC Model

## Slide 34: Build a Minimal HEC Model

## Slide 35: Run the HEC Model

## Slide 36: SWMM as Hydrologic Model
Now have SCS Type II in HEC-HMS, only after the two columns in the time series
Now go to the SWMM model and build a raingage to accept the time series

## Slide 37: SWMM Raingage

## Slide 38: SWMM as Hydrologic Model
Now copy-paste from HMS to SWMM the two columns
  Edit to fix the first value
  Edit to fix the 24th and 25th hours
  Set the time window
  Run SWMM

## Slide 39: SWMM as Hydrologic Model
Done! Interpret results

## Slide 40: SWMM as Hydrologic Model
Showed how to use HMS to generate SWMM input.
SWMM is also handy for generating HMS input
  the time arithmetic is more demanding!

## Slide 41: Next Time
Conduits in swmm
  Invert elevations and offsets
  Dual drainage systems